## Slide 1: Smart Bin System using ESP8266
Air Quality, Water Level, and Smart Bin Automation with Blynk Integration

## Slide 2: Overview
This Smart Bin project uses ESP8266 to monitor:
- Air Quality (MQ-135 Sensor)
- Water Level in the bin (Ultrasonic Sensor)
- Automatic Lid Opening (Ultrasonic + Servo Motor)
- Relay Control via Blynk (Manual Switch)
- All data displayed on LCD and sent to Blynk app

## Slide 3: Hardware Components
- NodeMCU ESP8266
- MQ-135 Gas Sensor
- Ultrasonic Sensors (2x)
- Servo Motor (SG90)
- Relay Module (controlled via V2)
- I2C LCD Display (16x2)
- Power Supply, Jumper Wires, Breadboard

## Slide 4: System Features
- Manual Relay Activation using Blynk (V2)
- Real-time Air Quality Display on LCD
- Water Level Monitoring with % calculation
- Bin Lid opens if object ≤ 5 cm using Servo
- All sensor values transmitted to Blynk

## Slide 5: Pin Configuration (ESP8266)
- MQ135 A0 → A0 (analog), MQ135 D0 → D0 (digital)
- Ultrasonic Water Level: Trig → D3, Echo → D4
- Ultrasonic Bin: Trig → D5, Echo → D6
- Servo → D7
- Relay → D8 (controlled via V2)
- LCD (I2C) → SDA: D2, SCL: D1

## Slide 6: Summary
This integrated Smart Bin project showcases:
- IoT-based monitoring
- Efficient waste management
- Real-time remote control and alerts
- Compact and low-power embedded solution